## Slide 1: SubNeTTING

## Slide 2: Definition
Subnetwork, or subnet, is a logically visible, distinctly addressed part of a single Internet Protocol network.
Subnetting is the division of a computer network into groups of computers that have a common, designated IP address routing prefix.

## Slide 3: Advantages
Allows a single shared network address to split it up into many smaller networks.
Without subnets, organizations would require many network addresses
  Limited number of Network addresses available
Alleviates traffic
  Smaller routing tables
  Alleviates excessive packet collision and congestion
Easier to manage and solve problems
Better Security
  Separating departments with highly sensitive material
    Accounting and Administration

## Slide 4: Disadvantages
Doesn’t allocate IP address proportionately per subnet
Limited by the number of IP address
Need to buy hardware such as routers

## Slide 5: Subnet Applications
Anywhere a large group of computers are located.

## Slide 6: IP Addressing Classes
Class A - 0nnnnnnn.hhhhhhhh.hhhhhhhh.hhhhhhhh
Initial byte = 0-127 (7 bits)
1.0.0.0 – 127.255.255.255
Class B - 10nnnnnn.nnnnnnnn.hhhhhhhh.hhhhhhhh
Initial byte = 128-191 (14 bits)
128.0.0.0 – 191.255.255.255
Class C - 100nnnnn.nnnnnnnn.nnnnnnnn.hhhhhhhh
Initial byte = 192-223 (21 bits)
192.0.0.0 – 223.255.255.255
n = network address h = host address

## Slide 7: Subnetting Your Network
Every IP address has a Subnet Mask.
172.16.25.2 255.255.0.0
Classless Interdomain Routing(CIDR)
172.16.25.2 /16

## Slide 8: Subnet Mask
Determines the way an IP address is split into network and hosts portions
Class A - 0nnnnnnn.hhhhhhhh.hhhhhhhh.hhhhhhhh
Subnet Mask = 255.0.0.0 IP Address /8
Class B - 10nnnnnn.nnnnnnnn.hhhhhhhh.hhhhhhhh
Subnet Mask = 255.255.0.0 IP Address /16
Class C - 100nnnnn.nnnnnnnn.nnnnnnnn.hhhhhhhh
Subnet Mask = 255.255.255.0 IP Address /24

## Slide 9: SubNetted Networks
The network portion of the address is extended by splitting up the host number
Borrowing 1 or more bits from the host bit portion

## Slide 10: Example:
Dividing a network into 2 subnets requires to borrow 1 bit
Class C:
11111111.11111111.11111111.10000000(255.255.255.128)
CIDR IP address /25
This would allow 126 hosts per subnet
All 1’s are reserved for broadcast ID
All 0’s are reserved for network ID

## Slide 11: Class C Subnetting
# of Subnets | # of Hosts/Subnet | NetMask | 4th Octet | CIDR Notation
2 | 126 | 255.255.255.128 | 10000000 | /25
4 | 62 | 255.255.255.192 | 11000000 | /26
8 | 30 | 255.255.255.224 | 11100000 | /27
16 | 14 | 255.255.255.240 | 11110000 | /28
32 | 6 | 255.255.255.248 | 11111000 | /29
64 | 2 | 255.255.255.252 | 11111100 | /30

## Slide 12
192.168.5.130 /24
Subnet mask = 255.255.255.0
4 Subnets = 62 hosts/subnet
Borrow 2 bits from host byte
Subnet A -> 192.168.5.1/26
to 192.168.5.62/26
Subnet B -> 192.168.5.65/26
to 192.168.5.126/26
Subnet C -> 192.168.5.129/26
to 192.168.5.190/26
Subnet D -> 192.168.5.193/26
to 192.168.5.254/26
192.168.5.0 = Network ID
Subnet Mask = 255.255.255.192
= /26

## Slide 13: Subnetting a Class C Network
The first three octets of a Class C address identifies the network number.
For example, 192.1.2.0
The fourth octet identifies the host address on this particular network.
The range of numbers for the fourth octet is 0 to 255.

## Slide 14: Subnetting a Class C Network
Two numbers in the fourth octet are reserved and cannot be assigned to a host (computer, printer, router, etc.)‏
The two addresses are 0 and 255.
0 identifies the network and 255 is the broadcast address for this network.

## Slide 15: Subnetting a Class C Network
Therefore, for network 192.1.2.0 the possible addresses are as follows:
192.1.2.0 is the major network address
192.1.2.1 to 192.1.2.254 are assignable host addresses
192.1.2.255 is the major broadcast address for this network.

## Slide 16: Subnetting a Class C Network
First you must determine the reason you are subnetting a network.
There are many reasons. We will choose one.
If we put all 254 hosts on this one major network, and the bandwidth is 100 Mbps, each host will have approximately 393,700 bps of bandwidth (~394 kbps)‏

## Slide 17: Subnetting a Class C Network
Suppose that we wish to give 4 Mbps of bandwidth to each user,
Then we will subnet the network and put a maximum of 25 users on each subnet.

## Slide 18: Subnetting a Class C Network
Aim: maximum of 25 users or hosts
Add 2 the the total number of users.
Write this chart.
128 64 32 16 8 4 2 1
It is the same chart we used earlier for number conversions.

## Slide 19: Subnetting a Class C Network
Locate between which two numbers where 27 is located.
128 64 32 16 8 4 2 1
^
27 is located between 16 and 32.
Note: After adding 2 to the number of workstations and the result is 4, 16, 32, 64, etc, draw the line to the right of that number.

## Slide 20: Subnetting a Class C Network
Draw a line between 16 and 32 as shown.
128 64 32 | 16 8 4 2 1
|
The three bits left of the vertical line will be used for the subnetwork number.
The five bits to the right of the line will be used for the host address.

## Slide 21: Subnetting a Class C Network
Place 1s below the three bots to the left of the line
Place 0s below the five bits to the right of the line
128 64 32 | 16 8 4 2 1
1 1 1 | 0 0 0 0 0
Remember, this is the fourth octet.

## Slide 22: Determining the Subnet Mask
The default mask for a class C address is 255.255.255.0
The 255.255.255 identifies the part of the subnet mask used for identifying the network portion of the IP address
The .0 identifies the host portion of the IP address.

## Slide 23: Determining the Subnet Mask
Start by writing the first three octets for the subnet mask: 255.255.255.
Now calculate the subnet mask number for the fourth octet
128 64 32 | 16 8 4 2 1
1 1 1 | 0 0 0 0 0
128 + 64 + 32 = ?

## Slide 24: Determining the Subnet Mask
Start by writing the first three octets for the subnet mask: 255.255.255.
Now calculate the subnet mask number for the fourth octet
128 64 32 | 16 8 4 2 1
1 1 1 | 0 0 0 0 0
128 + 64 + 32 = 224
Therefore the subnet mask is 255.255.255.224

## Slide 25: Addresses
The last steps.
Calculate each subnet address
Calculate the 1st host address
Calculate the last host address
Calculate the broadcast address for each subnetwork

## Slide 26: Addresses
The first subnetwork address is always 0.
192.1.2.0
For this example, the subnetwork address will increment by 32. 32 is the smallest part of the subnetwork address.
128 64 32 | 16 8 4 2 1
1 1 1 | 0 0 0 0 0

## Slide 27: Subnet Addresses
128 64 32 | 16 8 4 2 1
1 1 1 | 0 0 0 0 0
Subnet Addresses
0- 192.1.2.0 4- 192.1.2.128
1- 192.1.2.32 5- 192.1.2.160
2- 192.1.2.64 6- 192.1.2.192
3- 192.1.2.96 7- 192.1.2.224

## Slide 28: 1st Host Addresses
The first host address is always the subnet address plus 1.
For example: 192.1.2.0 + 1 = 192.1.2.1
Therefore the first host address is 192.1.2.1

## Slide 29: 1st Host Addresses
128 64 32 | 16 8 4 2 1
x x x | 0 0 0 0 1
1st host Addresses
0- 192.1.2.1 4- 192.1.2.129
1- 192.1.2.33 5- 192.1.2.161
2- 192.1.2.65 6- 192.1.2.193
3- 192.1.2.97 7- 192.1.2.225

## Slide 30: 1st Host Addresses
128 64 32 | 16 8 4 2 1
x x x | 0 0 0 0 1
1st host Addresses
0- 192.1.2.1 4- 192.1.2.129
1- 192.1.2.33 5- 192.1.2.161
2- 192.1.2.65 6- 192.1.2.193
3- 192.1.2.97 7- 192.1.2.225

## Slide 31: Broadcast Addresses
The broadcast address is always 1 less than the next subnetwork address.
For example, the broadcast address for subnet 0 can be calculated by subtracting 1 from the next subnetwork address.
192.1.2.32 – 1 = ?
Therefore the broadcast address for subnet 0 is 192.1.2.32 – 1 = 192.1.2.31

## Slide 32: Broadcast Addresses
128 64 32 | 16 8 4 2 1
x x x | 1 1 1 1 1
1st host Addresses
0- 192.1.2.31 4- 192.1.2.159
1- 192.1.2.63 5- 192.1.2.191
2- 192.1.2.95 6- 192.1.2.223
3- 192.1.2.127 7- 192.1.2.255

## Slide 33: Last Host Addresses
The last set of addresses to calculate are the the last available host addresses.
Using the broadcast address for each subnetwork, subtract 1 to obtain the last host address.
For example: broadcast address for subnet 0 is 192.1.2.31
The last host address is 192.1.2.30

## Slide 34: Last Host Addresses
128 64 32 | 16 8 4 2 1
x x x | 1 1 1 1 0
1st host Addresses
0- 192.1.2.30 4- 192.1.2.158
1- 192.1.2.62 5- 192.1.2.190
2- 192.1.2.94 6- 192.1.2.222
3- 192.1.2.126 7- 192.1.2.254